Architecture, history,
standards, and trends
Today, the Internet and World Wide Web (WWW) are familiar terms to millions of
people all over the world. Many people depend on applications enabled by the
Internet, such as electronic mail and Web access. In addition, the increase in
popularity of business applications places additional emphasis on the Internet.
The Transmission Control Protocol/Internet Protocol (TCP/IP) protocol suite is
the engine for the Internet and networks worldwide. Its simplicity and power has
led to its becoming the single network protocol of choice in the world today. In
this chapter, we give an overview of the TCP/IP protocol suite. We discuss how
the Internet was formed, how it developed, and how it is likely to develop in the
future.
1
4 TCP/IP Tutorial and Technical Overview
1.1 TCP/IP architectural model
The TCP/IP protocol suite is so named for two of its most important protocols:
Transmission Control Protocol (TCP) and Internet Protocol (IP). A less used
name for it is the Internet Protocol Suite, which is the phrase used in official
Internet standards documents. In this book, we use the more common, shorter
term, TCP/IP, to refer to the entire protocol suite.
1.1.1 Internetworking
The main design goal of TCP/IP was to build an interconnection of networks,
referred to as an internetwork, or internet, that provided universal
communication services over heterogeneous physical networks. The clear
benefit of such an internetwork is the enabling of communication between hosts
on different networks, perhaps separated by a large geographical area.
The words internetwork and internet are simply a contraction of the phrase
interconnected network. However, when written with a capital “I”, the Internet
refers to the worldwide set of interconnected networks. Therefore, the Internet is
an internet, but the reverse does not apply. The Internet is sometimes called the
connected Internet.
The Internet consists of the following groups of networks:
_ Backbones: Large networks that exist primarily to interconnect other
networks. Also known as network access points (NAPs) or Internet Exchange
Points (IXPs). Currently, the backbones consist of commercial entities.
_ Regional networks connecting, for example, universities and colleges.
_ Commercial networks providing access to the backbones to subscribers, and
networks owned by commercial organizations for internal use that also have
connections to the Internet.
_ Local networks, such as campus-wide university networks.
In most cases, networks are limited in size by the number of users that can
belong to the network, by the maximum geographical distance that the network
can span, or by the applicability of the network to certain environments. For
example, an Ethernet network is inherently limited in terms of geographical size.
Therefore, the ability to interconnect a large number of networks in some
hierarchical and organized fashion enables the communication of any two hosts
belonging to this internetwork.
Chapter 1. Architecture, history, standards, and trends 5
Figure 1-1 shows two examples of internets. Each consists of two or more
physical networks.
Figure 1-1 Internet examples: Two interconnected sets of networks, each seen as one
logical network
Another important aspect of TCP/IP internetworking is the creation of a
standardized abstraction of the communication mechanisms provided by each
type of network. Each physical network has its own technology-dependent
communication interface, in the form of a programming interface that provides
basic communication functions (primitives). TCP/IP provides communication
services that run between the programming interface of a physical network and
user applications. It enables a common interface for these applications,
independent of the underlying physical network. The architecture of the physical
network is therefore hidden from the user and from the developer of the
application. The application need only code to the standardized communication
abstraction to be able to function under any type of physical network and
operating platform.
As is evident in Figure 1-1, to be able to interconnect two networks, we need a
computer that is attached to both networks and can forward data packets from
one network to the other; such a machine is called a router. The term IP router is
also used because the routing function is part of the Internet Protocol portion of
the TCP/IP protocol suite (see 1.1.2, “The TCP/IP protocol layers” on page 6).
Two networks interconnected by a router equals Internet A
Router
R
One
Virtual
Network
Network 1 Network 2
Router
Network 1 R Network 2 Network 3
Router
R
Multiple networks interconnected by routers
(also seen as 1 virtual network, an Internet)
6 TCP/IP Tutorial and Technical Overview
To be able to identify a host within the internetwork, each host is assigned an
address, called the IP address. When a host has multiple network adapters
(interfaces), such as with a router, each interface has a unique IP address. The
IP address consists of two parts:
IP address = <network number><host number>
The network number part of the IP address identifies the network within the
internet and is assigned by a central authority and is unique throughout the
internet. The authority for assigning the host number part of the IP address
resides with the organization that controls the network identified by the network
number. We describe the addressing scheme in detail in 3.1.1, “IP addressing”
on page 68.
1.1.2 The TCP/IP protocol layers
Like most networking software, TCP/IP is modeled in layers. This layered
representation leads to the term protocol stack, which refers to the stack of
layers in the protocol suite. It can be used for positioning (but not for functionally
comparing) the TCP/IP protocol suite against others, such as Systems Network
Architecture (SNA) and the Open System Interconnection (OSI) model.
Functional comparisons cannot easily be extracted from this, because there are
basic differences in the layered models used by the different protocol suites.
By dividing the communication software into layers, the protocol stack allows for
division of labor, ease of implementation and code testing, and the ability to
develop alternative layer implementations. Layers communicate with those
above and below via concise interfaces. In this regard, a layer provides a service
for the layer directly above it and makes use of services provided by the layer
directly below it. For example, the IP layer provides the ability to transfer data
from one host to another without any guarantee to reliable delivery or duplicate
suppression. Transport protocols such as TCP make use of this service to
provide applications with reliable, in-order, data stream delivery.

1.4 Future of the Internet
Trying to predict the future of the Internet is not an easy task. Few would have
imagined, even five years ago, the extent to which the Internet has now become
a part of everyday life in business, homes, and schools. There are a number of
things, however, about which we can be fairly certain.
1.4.1 Multimedia applications
Bandwidth requirements will continue to increase at massive rates; not only is
the number of Internet users growing rapidly, but the applications being used are
becoming more advanced and therefore consume more bandwidth. New
technologies such as dense wave division multiplexing (DWDM) are emerging to
meet these high bandwidth demands being placed on the Internet.
Much of this increasing demand is attributable to the increased use of multimedia
applications. One example is that of Voice over IP technology. As this technology
matures, we are almost certain to see a sharing of bandwidth between voice and
data across the Internet. This raises some interesting questions for phone
companies. The cost to a user of an Internet connection between Raleigh, NC
and Santiago, Chile is the same as a connection within Raleigh, not so for a
traditional phone connection. Inevitably, voice conversations will become video
conversations as phone calls become video conferences.
Today, it is possible to hear radio stations from almost any part of the globe
through the Internet with FM quality. We can watch television channels from all
around the world, leading to the clear potential of using the Internet as the
vehicle for delivering movies and all sorts of video signals to consumers
everywhere. It all comes at a price, however, as the infrastructure of the Internet
must adapt to such high bandwidth demands.
1.4.2 Commercial use
The Internet has been through an explosion in terms of commercial use. Today,
almost all large business depend on the Internet, whether for marketing, sales,
customer service, or employee access. These trends are expected to continue.
Electronic stores will continue to flourish by providing convenience to customers
that do not have time to make their way to traditional stores.
Businesses will rely more and more on the Internet as a means for
communicating branches across the globe. With the popularity of virtual private
networks (VPNs), businesses can securely conduct their internal business over a
wide area using the Internet; employees can work from home offices yielding a
Chapter 1. Architecture, history, standards, and trends 27
virtual office environment. Virtual meetings probably will be common
occurrences.
1.4.3 The wireless Internet
Perhaps the most widespread growth in the use of the Internet, however, is that
of wireless applications. Recently, there has been an incredible focus on the
enablement of wireless and pervasive computing. This focus has been largely
motivated by the convenience of wireless connectivity. For example, it is
impractical to physically connect a mobile workstation, which by definition, is free
to roam. Constraining such a workstation to some physical geography simply
defeats the purpose. In other cases, wired connectivity simply is not feasible.
Examples include the ruins of Macchu Picchu or offices in the Sistine Chapel. In
these circumstances, fixed workstations also benefit from otherwise unavailable
network access.
Protocols such as Bluetooth, IEEE 802.11, and Wireless Application Protocol
(WAP) are paving the way toward a wireless Internet. While the personal
benefits of such access are quite advantageous, even more appealing are the
business applications that are facilitated by such technology. Every business,
from factories to hospitals, could enhance their respective services. Wireless
devices will become standard equipment in vehicles, not only for the personal
enjoyment of the driver, but also for the flow of maintenance information to
your favorite automobile mechanic. The applications are limitless.

10.1 Wireless concepts
Given the diverse nature of wireless implementation, there are a number of terms
and concepts relating to the wireless ideology. This section reviews some of the
more common of these.
Radio propagation
Radio propagation refers to the behavior exhibited by radio waves as they are
transmitted to and from points around the earth, and includes aspects such as
aurora, backscatter, and tropospheric scatter.
The decibel (dB)
Signal strength of radio waves is measured in decibels (dBs), specifically by
quantifying the amount of signal lost between two points in a wireless network.
This measurement is calculated as the difference between a signal’s strength at
an originating point and at a destination point. Changes in signal strengths are
measured in terms of positive or negative dB gain.
Path loss
Path loss refers to a signal’s loss in electromagnetic radiation as it propagates
from one point to another. Though this reduction can be directly affected by
things such as terrain and the environment, the actual loss is inversely
proportional to the distance travelled by the signal, and directly proportional to
the wave length of the signal.
Effective isotropic radiated power
Effective isotropic radiated power (ERP) is used to quantify the signal strength
produced by an antenna. It accounts for both the gain of the antenna as well as
the power that feeds into the antenna.
For example, if an antenna has -13 dB gain, and is fed by 100 dB, its ERP is 87
dB, as illustrated in Figure 10-1.
Figure 10-1 ERP example
Antenna gain
-13 dB
Power
100 dB
ERP = 100 dB -13 dB = 87 dB
Chapter 10. Wireless IP 393
Fixed versus mobile wireless
There are two types of wireless devices: fixed and mobile. Fixed devices are
stationary and draw their power from a utility main. An example of such a device
is a wireless router plugged into a wall outlet. Conversely, mobile devices are
those that have the capability of movement. Naturally, these are powered from
batteries. An example of this is a mobile computer.
Effects of multipath
Similar to a wired IP network, it is possible for radio signals to traverse different
paths between a source and destination. This can occur when one signal
encounters an obstruction. This can introduce delays into the traversal of signals
and is called multipath distortion.
System operating margin
The system operating margin defines the range in which error free reception is
achieved. This is calculated in dB as the difference between the received signal
level and the receiver’s sensitivity. For example, if the received signal is -15 dB,
and the sensitivity of the receiver is -10 dB, the system operating margin is 5 dB.
Free space loss
Free space loss is similar to path loss, except that path loss is experienced
between any two radio points and thus incorporates signal loss through various
types of media. Conversely, free space loss is specific to the lessening of a
signal as it traverses free space.
Decibel over isotropic (dBi)
Before decibel isotropic (dBi) units can be understood, the concept of an
isotropic antenna must first be explained. An isotropic antenna is theoretical, and
produces uniform signal strength in every direction, called isotropic radiation.
This sphere can then be used as a point of reference when measuring an actual
antenna’s strength. This measurement is made in units of dBi, and compares the
antenna’s strength relative to the isotropic radiation that would be created by an
isotropic antenna of the same strength. This is illustrated in Figure 10-2 on
page 394.
394 TCP/IP Tutorial and Technical Overview
Figure 10-2 Decibel over isotropic
Fresnel zone clearance
When obstructions exist within the path of a signal, diffraction of the signal
creates a series of concentric elliptical zones, each zone varying in signal
strength. Each of these zones represents a different Fresnel zone within the
signal. Fresnel zones are numbered outward from the center, and referred to as
the nth zone. This is illustrated in Figure 10-3. Note that the first zone has no
obstructions, providing the strongest signal to the house. The second zone was
created by tree obstructions and carries a signal weaker than the first zone, but
stronger than the third. The third zone, with the weakest signal, was the result of
an obstructing building.
Figure 10-3 An example of Fresnel zones
Isotropic radiation
Actual radiation dBi
measurement
Chapter 10. Wireless IP 395
Line of sight (LOS) and non-line of sight (NLOS) service
Line of sight (LOS) and non-line of sight (NLOS) are used to define a link by its
position relative to a signal’s transmitter. An LOS link is one that must have an
unobstructed path between it and the signal’s source, literally meaning that the
link has a line of site to the source. This usually indicates that the link is within the
first Freznel zone. If a link that requires LOS service moves into the second or
third zone (for example, where the person in Figure 10-3 on page 394 is
standing), it would no longer have LOS, and might not operate. However, a link
that can use NLOS would still operate correctly.
Wireless access point
Wireless access points typically relay data between wireless devices and a wired
network. However, multiple access points can be chained together, creating a
larger network to allow roaming of mobile devices.
Wireless router
A wireless router acts as a wireless access point combined with an Ethernet hub,
forwarding packets between a wireless subnet and any other subnet.
Wireless Ethernet bridge
Wireless Ethernet bridges connect two separate wireless networks without
requiring the services of a router.

10.2 Why wireless?
Though the immediate benefit implementing a wireless network (mobility) might
seem obvious, there are other benefits that might not be as readily evident.
10.2.1 Deployment and cost effectiveness
When creating a traditional, wired network, much of the construction centers
around laying cable. Though this is not as difficult a task when the network is
built in parallel with a structure, installing wired networks into existing structures
can be quite difficult because the wires must often be installed behind or above
solid walls or ceilings. This can incur substantial costs, both in purchasing the
wire as well as in paying for the construction to install the wire. When installed,
there is also the cost of maintaining the wires, which can degrade over time.
Conversely, creating a wireless network requires minimum construction, if any at
all. When building a large-scale network, there might be some initial cost and
construction to build antennas, access points, and so on. However, once built,
396 TCP/IP Tutorial and Technical Overview
the maintenance required by such structures is minimal. Additionally, there is no
cost for laying cable, which is significant on a large-scale network.
For small-scale networks (such as office buildings), the cost is relatively minimal.
Only access points (such as wireless routers) need to be purchased, and can
create their own network or be hooked into an existing network. There is no
construction cost, no cost for wiring, and therefore no cost in installing the wiring.
Additionally, such a network can be set up and configured in as fast as a day,
depending on the complexity of the organization’s needs.
10.2.2 Reachability
Wired networks do not lend themselves to certain geographies. For example,
imagine laying cable to provide connectivity between research stations in the
Amazon, or to interconnect remote communities in sparsely populated regions of
Wyoming. Not only would the wiring be costly, but the terrain through which the
cable must be laid might be prohibitive. For example, wet or hot climates (such
as the Amazon) might cause cabling to deteriorate too fast. Rocky terrains might
not be cost effective to bury the cable. Additionally, when the distance between
connected points is too great, the signal might degrade before the distance is
spanned. This, of course, can be resolved using repeaters, but this adds
additional costs.
Implementation of a wireless network can overcome these challenges simply
because it nullifies the need for wiring. Distances between nodes can be
spanned easily and the nuances of a terrain can be overcome. Additionally, if a
wired network is desired, wireless can be used to interconnect remote wired
networks.
10.2.3 Scalability
A common challenge faced by growing businesses is outgrowing their network.
When first constructing a network, a young business might not have an accurate
forecast of the network size needed to accommodate the organization. Then, as
the business needs grow, the network is no longer capable of supporting its
needs. As described previously, adding additional wiring might be cost
prohibitive and might compromise the success of the business.
In such a scenario, wireless networks can offer two solutions. First, wireless
capability can be added to an existing wired network. This allows the network to
grow as needed, and additions can continue to be made if the needs continue to
grow. Second, if the business initially builds a wireless network, the problematic
scenario will never occur because the organization can continue to add wireless
capability to address growing needs.
Chapter 10. Wireless IP 397
10.2.4 Security
One concern over any network is the question of security. As data becomes
more sensitive, and more readily available online, the need to protect this data
increases rapidly. A common misconception is that hackers or malicious users
are facilitated by the growing use of wireless because this allows them to steal
data having only proximity to a network.
However, with such a concern in mind, the wireless architectures and
technologies were designed specifically with security in mind. As such, wireless
networks are often more secure, through the use of advanced authentication and
encryption methods, than their wired counterparts.
10.2.5 Connectivity and reliability
Depending on the design and configuration of a wireless network, it is possible
that such a network might be prone to the same connectivity outages as a wired
network. However, this is a limitation of the design of a particular network and not
of the wireless architecture itself. For example, wireless networking lends itself to
the concept of mesh networking, described in 10.5.3, “Mesh networking” on
page 402. Through such an implementation, as nodes become available or are
removed from a network, the overall wireless network can “heal” itself, and still
provide connectivity to all of the other nodes.